Civic Hybrid Sedan Specification 2009

| Engineering |
| --- |
|  | Hybrid |
| Engine Type | In-Line 4-Cylinder |
| Engine Block/Cylinder Head | Aluminum-Alloy |
| Displacement (cc) | 1339 |
| Horsepower @ rpm (SAE net) | 110 @ 6000 |
| Torque (lb-ft @ rpm) | 123 @ 1000-2500 |
| Redline (rpm) | 6300 |
| Bore and Stroke (mm) | 73 x 80 |
| Compression Ratio | 10.8:1 |
| Valve Train | 8-Valve SOHC i-VTEC® |
| Multi-Point Fuel Injection | Standard |
| Drive-by-Wire™ Throttle System | Standard |
| Front-Wheel Drive | Standard |
| CARB Emissions Rating | AT-PZEV |
| Direct Ignition System with Immobilizer | Standard |
| 100K +/- Miles No Scheduled Tune-Ups* | Standard |
| Electric Motor / Generator |
|  | Hybrid |
| Permanent Magnet Motor | Standard |
| Electric Power Storage |
|  | Hybrid |
| Nickel Metal Hydride (Ni-MH) Battery | Standard |
| Output (Volts) | 158 |
| Transmissions |
|  | Hybrid |
| Continuously Variable Transmission (CVT) | Standard |
| Gear Ratios: 2.526~0.421, Reverse: 4.511~1.875, Final Drive: 4.94 |  |
| Body/Suspension/Chassis |
|  | Hybrid |
| Unit-Body Construction | Standard |
| MacPherson Strut Front Suspension | Standard |
| Multi-Link Rear Suspension | Standard |
| Stabilizer Bar (mm, front/rear) | 24.2 / 12.0 |
| Power-Assisted Rack-and-Pinion Steering | Electric |
| Steering Wheel Turns, Lock-to-Lock | 2.71 |
| Steering Ratio | 13.52 |
| Turning Diameter, Curb-to-Curb (ft) | 34.8 |
| Power-Assisted Ventilated Front Disc/Solid Rear Disc Brakes (in, front/rear) | 10.3 / 10.2 |
| Wheels | 15" Lightweight Alloys |
| All-Season Tires | P195 / 65 R15 89S |
| Compact Spare Tire | Standard |
| Exterior Measurements |
|  | Hybrid |
| Wheelbase (in) | 106.3 |
| Length (in) | 177.3 |
| Height (in) | 56.3 |
| Width (in) | 69.0 |
| Track (in, front/rear) | 59.1 / 60.2 |
| Curb Weight (lbs, AT) | 2877 |
| Weight Distribution (%, front/rear, AT) | 59 / 41 |
| Interior Measurements |
|  | Hybrid |
| Headroom (in, front/rear) | 39.4 / 37.4 |
| Legroom (in, front/rear) | 42.2 / 34.6 |
| Shoulder Room (in, front/rear) | 53.6 / 52.3 |
| Hiproom (in, front/rear) | 51.9 / 51.0 |
| Cargo Volume (cu ft) | 10.4 |
| Passenger Volume (cu ft) | 90.9 |
| Seating Capacity | 5 |
| EPA Mileage Estimates†/Capacities |
|  | Hybrid |
| CVT (City/Highway/Combined) | 40 / 45 / 42 |
| Crankcase (qt) | 4.0 |
| Coolant System (qt, MT/AT) | NA / 6.1 (CVT) |
| Fuel (gal) | 12.3 |
| Required Fuel | Regular Unleaded |
| Safety |
|  | Hybrid |
| 3-Point Seat Belts at all Seating Positions | Standard |
| Front 3-Point Seat Belts with Automatic Tensioning System | Standard |
| Driver's and Front Passenger's Seat Belt Reminder | Standard |
| Adjustable Front Seat Belt Anchors | Standard |
| Dual-Stage, Dual-Threshold Front Airbags (SRS) | Standard |
| Front Side Airbags with Passenger-Side Occupant Position Detection System (OPDS) | Standard |
| Side Curtain Airbags | Standard |
| Driver's and Front Passenger's Active Head Restraints | Standard |
| Advanced Compatibility Engineering™ (ACE™) Body Structure | Standard |
| Vehicle Stability Assist™ (VSA®) with Traction Control | Standard |
| Anti-Lock Braking System (ABS) | Standard |
| Electronic Brake Distribution (EBD) | Standard |
| Brake Assist | Standard |
| Tire Pressure Monitoring System (TPMS) | Standard |
| Daytime Running Lights (DRL) | Standard |
| Side-Impact Door Beams | Standard |
| Outboard Lower Anchors and Tethers for CHildren (LATCH) | Standard |
| Child-Proof Rear Door Locks | Standard |
| Emergency Trunk Release | Standard |
| Exterior Features |
|  | Hybrid |
| Integrated Rear-Window Antenna | Roof Mounted |
| Security System with Remote Entry | with Trunk Release |
| Body-Colored Power Side Mirrors | with Integrated Turn Indicators |
| Heated Side Mirrors | with Leather |
| Variable Intermittent Windshield Wipers | Standard |
| Rear Decklid Spoiler | Standard |
| Impact-Absorbing Body-Colored Bumpers | Standard |
| Multi-Reflector Halogen Headlights | Standard |
| Body-Colored Door Handles | Standard |
| Chrome Rear License Plate Trim | Standard |
| Comfort & Convenience |
|  | Hybrid |
| Air Conditioning with Air-Filtration System | Automatic Climate Control |
| Honda Satellite-Linked Navigation SystemTM with Voice Recognition** | Available |
| Bluetooth® HandsFreeLink®†† | with Navigation |
| Power Windows with Auto-Up/Down Driver's Window | Standard |
| Power Door Locks with Auto-Lock Feature | Standard |
| Cruise Control | Standard |
| Perforated Leather-Wrapped Steering Wheel | with Leather |
| Steering Wheel-Mounted Controls | Cruise/Audio/Navi(available) |
| Tilt and Telescopic Steering Column | Standard |
| Beverage Holders | Front |
| Center Console with Sliding Armrest and Storage Compartment | Standard |
| Front Door-Pocket Storage Bins | Standard |
| Passenger-Side Seatback Pocket | Driver- and Passenger-Side |
| Coin Tray | Standard |
| Satin-Finish Door-Handle Pulls | Standard |
| Remote Fuel Filler Door Release | Standard |
| Remote Trunk Release with Lock | Standard |
| Headlights-On Reminder | Standard |
| Driver's and Front Passenger's Vanity Mirrors | Standard |
| Map Lights | Standard |
| Rear-Seat Heater Ducts | Standard |
| Floor Mats | Standard |
| Driver's Footrest | Standard |
| 12-Volt Power Outlet | Front and Center Console |
| Rear Window Defroster with Timer | Standard |
| Cargo Area Light | Standard |
| Seating |
|  | Hybrid |
| Leather-Trimmed Interior | Available |
| Heated Front Seats | with Leather |
| Driver's Seat with Manual Height Adjustment | Standard |
| Reclining Front Seatbacks | Standard |
| Adjustable Head Restraints | Standard |
| Audio Systems |
|  | Hybrid |
| 160-Watt AM/FM//CD Audio System with 6 Speakers | Standard |
| MP3/Windows Media® Audio (WMA) Playback Capability | Standard |
| MP3/Auxiliary Input Jack | Standard |
| USB Audio Interface | Standard |
| XM® Radio** | with Navigation |
| CD Text Display Capability | Standard |
| Digital Audio-Card Reader | with Navigation |
| Speed-Sensitive Volume Control (SVC) | Standard |
| Instrumentation |
|  | Hybrid |
| Two-Tier Instrument Panel | Standard |
| Blue Backlit Gauges | with Electronic IMA Display |
| Tachometer | Standard |
| Digital Odometer and Digital Trip Meters (2) | Standard |
| Idle-Stop Indicator | Standard |
| Maintenance Minder™ System | Standard |
| Tire Pressure Monitoring System (TPMS) Indicator | Standard |
| Exterior Temperature Indicator | Standard |
| Digital Fuel-Mileage Indicators | Standard |
| IMA Charge and Assist Indicators | Standard |
| Average Fuel Consumption Indicator | Standard |
| Fuel and Coolant Temperature Indicators | Standard |
| Door/Trunk-Open Indicators | Standard |
| Low-Fuel and Low-Oil Pressure Indicators | Standard |
| Passenger-Side Side Airbag-Off Indicator | Standard |
| Front Passenger Airbag-Off Indicator | Standard |

* Does not apply to fluid and filter changes. Will vary with driving conditions. See your owner's manual for more details.

† Based on 2009 EPA mileage estimates, reflecting new EPA fuel economy methods beginning with 2008 models. Use for comparison purposes only. Do not compare to models before 2008. Your actual mileage will vary depending on how you drive and maintain your vehicle.

** The Honda Satellite-Linked Navigation System™ is available on the Civic Hybrid in the United States, except Alaska. See your Honda dealer for details.

†† The Bluetooth® word mark and logos are owned by the Bluetooth SIG, Inc., and any use of such marks by Honda Motor Co., Ltd., is under license.